## Slide 1: Ambient Intelligence
Mitja Luštrek
Jožef Stefan Institute Department of Intelligent Systems

## Slide 2: What is ambient intelligence (AmI)
Defined not by technology but by objectives → interdisciplinary
Environment should be sensitive and responsive to the users and their needs
No special skills and minimal interaction from the users needed
Technology disappears except for the user interface, its benefits remain

## Slide 3: What is ambient intelligence (AmI)
Defined not by technology but by objectives → interdisciplinary
Environment should be sensitive and responsive to the users and their needs
No special skills and minimal interaction from the users needed
Technology disappears except for the user interface, its benefits remain

## Slide 4: AmI in relation to other areas
Mobile and distributed computing
Sensing
Human-computer interaction
Artificial intelligence
AmI

## Slide 5: AmI in relation to other areas
Mobile and distributed computing
Human-computer interaction
Artificial intelligence
Sensing
AmI
Ubiquitous computing

## Slide 6: AmI in relation to other areas
Mobile and distributed computing
Human-computer interaction
Artificial intelligence
Sensing
AmI
Ubiquitous computing
Pervasive computing

## Slide 7: Common settings

## Slide 8: Wearables systems
Specialized devices (sensing, some processing)
Consumer wearables (sensing, some processing, HCI)
Smartphones (sensing, processing, HCI)
Images copyright Shimmer, Microsoft, Samsung

## Slide 9: Wearable sensors
Accelerometer: acceleration, including gravity → orientation
Gyroscope: angular velocity
Photoplethysmogram (PPG) sensor: blood volume pulse → heart activity, blood oxygen (multiple wavelenghts)
Electrocardiogram (ECG) sensor: heart activity (richer information than PPG)
Electromyogram (EMG) sensor: activity of other muscles
Images copyright Shimmer, Microsoft, Samsung

## Slide 10: Wearable sensors
Accelerometer: acceleration, including gravity → orientation
Gyroscope: angular velocity
Photoplethysmogram (PPG) sensor: blood volume pulse → heart activity, blood oxygen (multiple wavelenghts)
Electrocardiogram (ECG) sensor: heart activity (richer information than PPG)
Electromyogram (EMG) sensor: activity of other muscles
Images copyright Shimmer, Microsoft, Samsung

## Slide 11: Wearable sensors
Electroencephalogram (EEG) sensor: brain activity
Galvanic skin response (GSR) / electrodermal activity (EDA): skin conductivity → sweating
Temperature sensor: skin/ambient temperature
Air pressure sensor: air pressure → (change in) altitude
GPS: location
Images copyright Shimmer, Microsoft, Samsung

## Slide 12: Wearable sensors
Electroencephalogram (EEG) sensor: brain activity
Galvanic skin response (GSR) / electrodermal activity (EDA): skin conductivity → sweating
Temperature sensor: skin/ambient temperature
Air pressure sensor: air pressure → (change in) altitude
GPS: location
Images copyright Shimmer, Microsoft, Samsung

## Slide 13: Wearable sensors
Electroencephalogram (EEG) sensor: brain activity
Galvanic skin response (GSR) / electrodermal activity (EDA): skin conductivity → sweating
Temperature sensor: skin/ambient temperature
Air pressure sensor: air pressure → (change in) altitude
GPS: location
Images copyright Shimmer, Microsoft, Samsung

## Slide 14: Smart indoor environments
Smart homes/offices
Ambient assisted living (AAL) environments
Living laboratories
Special: smart factories, hospitals, shops...
Sensing, actuation; processing not an issue, various methods for HCI
Image copyright IEEE / Jaime Lloret et al.

## Slide 15: Smart indoor environments
Smart homes/offices
Ambient assisted living (AAL) environments
Living laboratories
Special: smart factories, hospitals, shops...
Sensing, actuation; processing not an issue, various methods for HCI
Image copyright IEEE / Jaime Lloret et al.

## Slide 16: Indoor sensors
Camera (sometimes infrared)
Passive infrared (PIR) sensor, pressure sensor: occupant movement
Door, window, water flow sensor
Temperature, humidity, CO2 sensor
Gas, carbon monoxide, flood sensor
Electricity meter: appliance use
Indoor localization – Bluetooth beacons, RFID, ultrasound, ultra-wideband ...

## Slide 17: Indoor sensors
Camera (sometimes infrared)
Passive infrared (PIR) sensor, pressure sensor: occupant movement
Door, window, water flow sensor
Temperature, humidity, CO2 sensor
Gas, carbon monoxide, flood sensor
Electricity meter: appliance use
Indoor localization – Bluetooth beacons, RFID, ultrasound, ultra-wideband ...

## Slide 18: Indoor sensors
Camera (sometimes infrared)
Passive infrared (PIR) sensor, pressure sensor: occupant movement
Door, window, water flow sensor
Temperature, humidity, CO2 sensor
Gas, carbon monoxide, flood sensor
Electricity meter: appliance use
Indoor localization – Bluetooth beacons, RFID, ultrasound, ultra-wideband ...

## Slide 19: Indoor sensors
Camera (sometimes infrared)
Passive infrared (PIR) sensor, pressure sensor: occupant movement
Door, window, water flow sensor
Temperature, humidity, CO2 sensor
Gas, carbon monoxide, flood sensor
Electricity meter: appliance use
Indoor localization – Bluetooth beacons, RFID, ultrasound, ultra-wideband ...

## Slide 20: Indoor sensors
Camera (sometimes infrared)
Passive infrared (PIR) sensor, pressure sensor: occupant movement
Door, window, water flow sensor
Temperature, humidity, CO2 sensor
Gas, carbon monoxide, flood sensor
Electricity meter: appliance use
Indoor localization – Bluetooth beacons, RFID, ultrasound, ultra-wideband ...

## Slide 21: Smart outdoor environments
Smart cities
Public displays
Farms
Natural environments
...

## Slide 22: Common applications

## Slide 23: Health and AAL
Monitoring and assisting elderly people at home and on the go
Monitoring and guiding chronic patients at home and on the go

## Slide 24: Health and AAL
Monitoring and assisting elderly people at home and on the go
Monitoring and guiding chronic patients at home and on the go
Monitoring hospital patients / nursing home residents

## Slide 25: Health and AAL
Monitoring and assisting elderly people at home and on the go
Monitoring and guiding chronic patients at home and on the go
Monitoring hospital patients / nursing home residents
Monitoring and encouraging physical activity and general wellbeing of healthy users

## Slide 26: Comfort, power and security
Controlling heating, ventilation, lighting etc. for higher comfort and lower power consumption
Appliance use scheduling for lower power consumption
Security monitoring – detection of unusual or prohibited behaviours/events

## Slide 27: Comfort, power and security
Controlling heating, ventilation, lighting etc. for higher comfort and lower power consumption
Appliance use scheduling for lower power consumption
Security monitoring – detection of unusual or prohibited behaviours/events

## Slide 28: Miscellaneous
Augmented reality in professional settings
Effective management of smart city infrastructure
Sensing and content adaptation for public displays
Sensing and actuation for precision agriculture
Monitoring natural environment for preservation and exploitation
...

## Slide 29: Miscellaneous
Augmented reality in professional settings
Effective management of smart city infrastructure
Sensing and content adaptation for public displays
Sensing and actuation for precision agriculture
Monitoring natural environment for preservation and exploitation
...

## Slide 30: Miscellaneous
Augmented reality in professional settings
Effective management of smart city infrastructure
Sensing and content adaptation for public displays
Sensing and actuation for precision agriculture
Monitoring natural environment for preservation and exploitation
...

## Slide 31: Common technolgies and methods

## Slide 32: ... by area
Mobile and distributed computing
Human-computer interaction
Artificial intelligence
Sensing
AmI

## Slide 33: Artificial intelligence
Mobile and distributed computing
Human-computer interaction
Sensing
AmI
Machine learning and symbolic reasoning to models events, users, activities ...
Ontologies to represent knowledge
Rules to represent actions
Artificial intelligence

## Slide 34: Sensing
Mobile and distributed computing
Human-computer interaction
Artificial intelligence
AmI
Computer vision
Indoor localization
Device-free sensing (from radio interference)
Sensing

## Slide 35: Mobile and distributed computing
Human-computer interaction
Artificial intelligence
Sensing
AmI
Internet of things
Middlewares (e.g., UniversAAL)
Mobile and distributed computing

## Slide 36: Human-computer interaction
Mobile and distributed computing
Artificial intelligence
Sensing
AmI
Gesture-based, tangible interaction
Augmented reality
User-centred design
Human-computer interaction

## Slide 37: Wearable example

## Slide 38: Overview of the example
Sensing:
Acceleration
Heart rate
GSR

## Slide 39: Overview of the example
Sensing:
Acceleration
Heart rate
GSR
Processing:
Activity recogniton
Human energy expenditure estimation
Stress detection

## Slide 40: Overview of the example
Sensing:
Acceleration
Heart rate
GSR
Processing:
Activity recogniton
Human energy expenditure estimation
Stress detection
Wellbeing recommendations:
Adequate daily/ weekly physical activity
Relaxation exercises if stressed

## Slide 41: Overview of the example
Sensing:
Acceleration
Heart rate
GSR
Processing:
Activity recogniton
Human energy expenditure estimation
Stress detection
Wellbeing recommendations:
Adequate daily/ weekly physical activity
Move each hour
Relaxation exercises if stressed

## Slide 42: Activity recognition
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
Sliding window (2 s)

## Slide 43: Activity recognition
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
Sliding window (2 s)
f1 | f2 | f3 | ... |  | Activity
Training
Machine learning
AR model
Average acceleration
Standard deviation of acceleration
Orientation
...

## Slide 44: Activity recognition
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
f1 | f2 | f3 | ... | 
Use/testing
Activity
Sliding window (2 s)
AR model

## Slide 45: Activity recognition
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
Activity
AR model

## Slide 46: Energy expenditure estimation
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate data
Sliding window (10 s)
Activity
AR model

## Slide 47: Energy expenditure estimation
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate data
Sliding window (10 s)
f’1 | f’2 | f’3 | ... |  | Activity | EE
Training
Machine learning (regression)
EEE model
Activity
AR model
Like for AR
Heart rate
Area under acceleration
Kinetic energy
...

## Slide 48: Energy expenditure estimation
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate data
Sliding window (10 s)
f’1 | f’2 | f’3 | ... |  | Activity
Use/testing
EEE model
Activity
AR model
EE

## Slide 49: Energy expenditure estimation
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate data
EEE model
EE

## Slide 50: Energy expenditure estimation
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate, GSR data
EEE model
EE
Sliding window (1 min)
f“1 | f“2 | f“3 | ... | History | Time | EE | Stress
Training
Machine learning (classification)
Heart rate variability features
GSR frequency features
Stress model

## Slide 51: Energy expenditure estimation
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate, GSR data
EEE model
EE
Sliding window (1 min)
f“1 | f“2 | f“3 | ... | History | Time | EE
Machine learning (classification)
Stress model
Use/testing
Stress

## Slide 52: Energy expenditure estimation
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate, GSR data
Sliding window (1 min)
Stress model
Stress

## Slide 53: Wellbeing monitoring
Stress
Stress model
Activity
AR model
EEE model
EE
Improvements:
Adaptation to the phone‘s location, orientation
Multiple models (for energy expenditure estimation, stress detection)
Deep learning
...

## Slide 54: Smart environment example

## Slide 55: Overview of the example
Sensing:
Hardware
Virtual
Image copyright Netatmo

## Slide 56: Overview of the example
Sensing:
Hardware
Virtual
Reason about:
Which sensor values are bad
Which actions improve them
Ontology +
Reasoning
Image copyright Netatmo

## Slide 57: Overview of the example
Sensing:
Hardware
Virtual
Reason about:
Which sensor values are bad
Which actions improve them
Simulation
Ontology +
Reasoning
Simulate suggested actions
Recommend the best one
Image copyright Netatmo

## Slide 58: Overview of the example
Sensing:
Hardware
Virtual
Reason about:
Which sensor values are bad
Which actions improve them
Simulation
Ontology +
Reasoning
Environment recommendations:
Appropriate temperature
Good air quality
Simulate suggested actions
Recommend the best one
Image copyright Netatmo

## Slide 59: Sensing
Sensing:
Hardware
Virtual
Indoor:
Temperature
Humidity
CO2
Outdoor:
Temperature
Humidity

## Slide 60: Sensing
Sensing:
Hardware
Virtual
Number of occupants
Windows opened/closed
Indoor:
Temperature
Humidity
CO2
Outdoor:
Temperature
Humidity

## Slide 61: Sensing
Sensing:
Hardware
Virtual
Number of occupants
Windows opened/closed
Hardware sensor readings (CO2 and others)
Machine-learning model / heuristics
Indoor:
Temperature
Humidity
CO2
Outdoor:
Temperature
Humidity

## Slide 62: Ontology + reasoning

## Slide 63: Simulation
Suggested actions
from the ontology + reasoning

## Slide 64: Simulation
Suggested actions
from the ontology + reasoning
Prediction of outcomes:
Temperature
Humidity
CO2

## Slide 65: Simulation
Suggested actions
from the ontology + reasoning
Prediction of outcomes:
Temperature
Humidity
CO2
History of sensor readings
Machine-learning / physics models

## Slide 66: Simulation
Suggested actions
from the ontology + reasoning
Prediction of outcomes:
Temperature
Humidity
CO2
Evaluation of the predicted outcomes

## Slide 67: Simulation
Suggested actions
from the ontology + reasoning
Prediction of outcomes:
Temperature
Humidity
CO2
Evaluation of the predicted outcomes
–1
0
1
0
–1

## Slide 68: Simulation
Suggested actions
from the ontology + reasoning
Prediction of outcomes:
Temperature
Humidity
CO2
Evaluation of the predicted outcomes
Recommended action