## Slide 1: Ambient Intelligence
Mitja Luštrek
Jožef Stefan Institute Department of Intelligent Systems

## Slide 2: What is ambient intelligence (AmI)
Defined not by technology but by objectives → interdisciplinary
Environment should be sensitive and responsive to the users and their needs
No special skills and minimal interaction from the users needed
Technology disappears except for the user interface, its benefits remain

## Slide 3: AmI in relation to other areas
Mobile and distributed computing
Human-computer interaction
Artificial intelligence
Sensing
AmI
Ubiquitous computing
Pervasive computing

## Slide 4: Common settings

## Slide 5: Wearables systems
Specialized devices (sensing, some processing)
Consumer wearables (sensing, some processing, HCI)
Smartphones (sensing, processing, HCI)
Images copyright Shimmer, Microsoft, Samsung

## Slide 6: Wearable sensors
Accelerometer: acceleration, including gravity → orientation
Gyroscope: angular velocity
Photoplethysmogram (PPG) sensor: blood volume pulse → heart activity, blood oxygen (multiple wavelenghts)
Electrocardiogram (ECG) sensor: heart activity (richer information than PPG)
Electromyogram (EMG) sensor: activity of other muscles
Images copyright Shimmer, Microsoft, Samsung, Bittium

## Slide 7: Wearable sensors
Galvanic skin response (GSR) / electrodermal activity (EDA): skin conductivity → sweating
Electroencephalogram (EEG) sensor: brain activity
Temperature sensor: skin/ambient temperature
Air pressure sensor: air pressure → (change in) altitude
GPS: location
Images copyright Shimmer, Microsoft, Samsung, BioSemi, MindWave

## Slide 8: Smart indoor environments
Smart homes/offices
Ambient assisted living (AAL) environments
Living laboratories
Special: smart factories, hospitals, shops...
Sensing, actuation
Processing not an issue
Various methods for HCI
Image copyright IEEE / Jaime Lloret et al.

## Slide 9: Indoor sensors
Camera (infrared)
Microphone
Passive infrared (PIR) sensor, pressure sensor: occupant movement
Door, window, water flow sensor
Temperature, humidity, CO2, air pressure sensor
Gas, carbon monoxide, flood sensor
Electricity meter: appliance use
Indoor localization – Bluetooth beacons, RFID, ultrasound, ultra-wideband ...

## Slide 10: Smart outdoor environments
Smart cities
Public displays
Farms
Natural environments
...

## Slide 11: Common applications

## Slide 12: Health, wellbeing and AAL
Monitoring and assisting elderly people at home and on the go
Monitoring and guiding chronic patients at home and on the go
Monitoring hospital patients / nursing home residents
Monitoring and encouraging physical activity and general wellbeing of healthy users

## Slide 13: Comfort, energy and security
Controlling heating, ventilation, lighting etc. for higher comfort and lower energy consumption
Appliance use scheduling for lower energy consumption
Security monitoring – detection of unusual or prohibited behaviours/events

## Slide 14: Miscellaneous
Affective computing
Management of smart city infrastructure
Sensing and content adaptation for public displays
Sensing and actuation for precision agriculture
Monitoring natural environment for preservation and exploitation
...

## Slide 15: Common technolgies and methods

## Slide 16: ... by area
Mobile and distributed computing
Human-computer interaction
Artificial intelligence
Sensing
AmI

## Slide 17: Artificial intelligence
Mobile and distributed computing
Human-computer interaction
Sensing
AmI
Machine learning and symbolic reasoning to models events, users, activities ...
Ontologies to represent knowledge
Rules to represent actions
Artificial intelligence

## Slide 18: Sensing
Mobile and distributed computing
Human-computer interaction
Artificial intelligence
AmI
Computer vision
Indoor localization
Device-free sensing (from radio interference)
Sensing

## Slide 19: Mobile and distributed computing
Human-computer interaction
Artificial intelligence
Sensing
AmI
Internet of things
Middlewares (e.g., UniversAAL)
Mobile and distributed computing

## Slide 20: Human-computer interaction
Mobile and distributed computing
Artificial intelligence
Sensing
AmI
Gesture-based, tangible interaction
Augmented reality
User-centred design
Human-computer interaction

## Slide 21: Wearable example

## Slide 22: Overview of the example
Sensing:
Acceleration
Heart rate
GSR
Processing:
Activity recogniton
Human energy expenditure estimation
Stress detection
Wellbeing recommendations:
Adequate daily/ weekly physical activity
Relaxation exercises if stressed

## Slide 23: Activity recognition
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
Sliding window (2 s)

## Slide 24: Activity recognition
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
Sliding window (2 s)
f1 | f2 | f3 | ... |  | Activity
Training
Machine learning
AR model
Average acceleration
Standard deviation of acceleration
Orientation
...
Manually
labelled

## Slide 25: Activity recognition
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
f1 | f2 | f3 | ... | 
Use/testing
Activity
Sliding window (2 s)
AR model

## Slide 26: Energy expenditure estimation
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate data
Sliding window (10 s)
Activity
AR model

## Slide 27: Energy expenditure estimation
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate data
Sliding window (10 s)
f’1 | f’2 | f’3 | ... |  | Activity | EE
Training
Machine learning (regression)
EEE model
Activity
AR model
Like for AR
Heart rate
Area under acceleration
Kinetic energy
...
Image copyright University of Porto

## Slide 28: Energy expenditure estimation
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate data
Sliding window (10 s)
f’1 | f’2 | f’3 | ... |  | Activity
Use/testing
EEE model
Activity
AR model
EE

## Slide 29: Stress detection
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate, GSR data
EEE model
EE
Sliding window (1 min)
f“1 | f“2 | f“3 | ... | History | Time | EE | Stress
Training
Machine learning (classification)
Heart rate variability features
GSR frequency features
Stress model
Image copyright QuestionPro

## Slide 30: Stress detection
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate, GSR data
EEE model
EE
Sliding window (1 min)
f“1 | f“2 | f“3 | ... | History | Time | EE
Machine learning (classification)
Stress model
Use/testing
Stress

## Slide 31: Wellbeing monitoring
Stress
Stress model
Activity
AR model
EEE model
EE
Improvements:
Adaptation to the phone‘s location, orientation
Multiple models (for energy expenditure estimation, stress detection)
Deep learning
...

## Slide 32: Smart environment example

## Slide 33: Overview of the example
Sensing:
Hardware
Virtual
Reason about:
Which sensor values are bad
Which actions improve them
Simulation
Ontology +
Reasoning
Environment recommendations:
Appropriate temperature
Good air quality
Simulate suggested actions
Recommend the best one
Image copyright Netatmo

## Slide 34: Sensing
Sensing:
Hardware
Virtual
Number of occupants
Windows opened/closed
Hardware sensor readings (CO2 and others)
Machine-learning model / heuristics
Indoor:
Temperature
Humidity
CO2
Outdoor:
Temperature
Humidity
Image copyright Netatmo

## Slide 35: Ontology + reasoning

## Slide 36: Simulation
Suggested actions
from the ontology + reasoning
Prediction of outcomes:
Temperature
Humidity
CO2
Evaluation of the predicted outcomes
Recommended action
–1
0
1
0
–1
History of sensor readings
Machine-learning / physics models

## Slide 37: Conclusion
Ambient intelligence = environment intelligently and unobtrusively responsive
Devices: wearable and ambient sensors ...
Methods: machine learning, symbolic reasoning, knowledge representation ...
Domains: health and wellbeing, comfort and energy consumption ...

## Slide 38: Literature (1)
Physical monitoring with wearable sensors + machine learning: Cvetković et al., Real-time activity monitoring with a wristband and a smartphone, Information Fusion 2018
Psychological monitoring with wearable sensors + machine learning: Gjoreski et al., Monitoring stress with a wrist device using context, Journal of Biomedical Informatics 2017
Ambient sensors + symbolic reasoning: Alirezaie et al., An ontology-based context-aware system for smart homes: E-care@home, Sensors 2017

## Slide 39: Literature (2)
Audio + deep learning: Georgiev et al., Low-resource multi-task audio sensing for mobile and embedded devices via shared deep neural network representations, Ubicomp 2017
Indoor localization: Zafari et al., A Survey of indoor localization systems and technologies, 2018
Internet of Things: Al-Fuqaha et al., Internet of Things: A survey on enabling technologies, protocols, and applications, IEEE Communication Surveys & Tutorials 2015

## Slide 40: Literature (3)
Human-computer interaction: Hui & Sherratt, Towards disappearing user interfaces for ubiquitous computing: Human enhancement from sixth sense to super senses, Journal of Ambient Intelligence and Humanized Computing 2017