## Slide 1: Ambient Intelligence
Mitja Luštrek
Jožef Stefan Institute Department of Intelligent Systems

## Slide 2: What is ambient intelligence (AmI)
Defined not by technology but by objectives → interdisciplinary
Environment should be sensitive and responsive to the users and their needs
No special skills and minimal interaction from the users needed
Technology disappears except for the user interface, its benefits remain

## Slide 3: AmI in relation to other areas
Mobile and distributed computing
Human-computer interaction
Artificial intelligence
Sensing
AmI
Ubiquitous computing
Pervasive computing
Internet of things

## Slide 4: Common settings

## Slide 5: Wearables systems
Specialized devices (sensing, some processing)
Consumer wearables (sensing, some processing, HCI)
Smartphones (sensing, processing, HCI)
Images copyright Shimmer, Microsoft, Samsung

## Slide 6: Wearable sensors
Accelerometer: acceleration, including gravity → orientation
Gyroscope: angular velocity → orientation
Magnetometer: magnetic field → orientation
Inertial sensors / inertial measurement unit (IMU)

## Slide 7: Wearable sensors
Photoplethysmogram (PPG) sensor: blood volume pulse → heart activity, blood oxygen (multiple wavelenghts)
Image copyright Innovo, University of Toronto

## Slide 8: Wearable sensors
Electrocardiogram (ECG) sensor: heart activity (richer information than PPG)
Electromyogram (EMG) sensor: activity of other muscles
Images copyright Zephyr, MathWorks, Agateller

## Slide 9: Wearable sensors
Galvanic skin response (GSR) / electrodermal activity (EDA): skin conductivity → sweating
Electroencephalogram (EEG) sensor: brain activity
Temperature sensor: skin/ambient temperature
Air pressure sensor: air pressure → (change in) altitude
GPS: location
Images copyright BioSemi, MindWave

## Slide 10: Smart indoor environments
Smart homes/offices
Ambient assisted living (AAL) environments
Living laboratories
Special: smart factories, hospitals, shops...
Sensing, actuation
Processing not an issue
Various methods for HCI
Image copyright IEEE / Lloret et al.

## Slide 11: Ambient sensors
Camera (infrared)
Image copyright Potdar et al., Simon Fraser University, Springer / Panasiti et el.

## Slide 12: Ambient sensors
Microphone: human activity, machine noise
Passive infrared (PIR) sensor, pressure sensor: human movement
Door, window, water flow sensor
Temperature, humidity, CO2, air pressure sensor
Gas, carbon monoxide, flood sensor
Electricity meter: appliance use

## Slide 13: Ambient sensors
Electronic nose: specific gases
Indoor localization – Bluetooth beacons, RFID, ultrasound, ultra-wideband ...
Image copyright Eliko

## Slide 14: Smart outdoor environments
Smart cities
Public displays
Farms
Natural environments
...

## Slide 15: Common applications

## Slide 16: Health, wellbeing and AAL
Monitoring and assisting elderly people at home and on the go
Monitoring and guiding chronic patients at home and on the go
Monitoring hospital patients / nursing home residents
Monitoring and encouraging physical activity and general wellbeing of healthy users

## Slide 17: Comfort, energy and security
Controlling heating, ventilation, lighting etc. for higher comfort and lower energy consumption
Appliance use scheduling for lower energy consumption
Security monitoring – detection of unusual or prohibited behaviours/events

## Slide 18: Miscellaneous
Affective computing
Sensing and actuation for managing smart city infrastructure and providing public services
Sensing and actuation for precision agriculture
Monitoring natural environment for preservation and exploitation
...

## Slide 19: Common technolgies and methods

## Slide 20: ... by area
Mobile and distributed computing
Human-computer interaction
Artificial intelligence
Sensing
AmI

## Slide 21: Artificial intelligence
Mobile and distributed computing
Human-computer interaction
Sensing
AmI
Machine learning and symbolic reasoning to models events, users, activities ...
Ontologies to represent knowledge
Rules to represent actions
Artificial intelligence

## Slide 22: Sensing
Mobile and distributed computing
Human-computer interaction
Artificial intelligence
AmI
Computer vision
Indoor localization
Radio-based sensing
Sensing

## Slide 23: Mobile and distributed computing
Human-computer interaction
Artificial intelligence
Sensing
AmI
Protocols
Middlewares (e.g., UniversAAL)
Mobile and distributed computing

## Slide 24: Human-computer interaction
Mobile and distributed computing
Artificial intelligence
Sensing
AmI
Gesture-based, tangible interaction
Augmented reality
User-centred design
Human-computer interaction

## Slide 25: Wearable example with classical machine learning

## Slide 26: Overview of the example
Sensing:
Acceleration
Heart rate
GSR
Processing:
Activity recogniton
Human energy expenditure estimation
Stress detection
Wellbeing recommendations:
Adequate daily/ weekly physical activity
Relaxation exercises if stressed

## Slide 27: Activity recognition
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
Sliding window (2 s)

## Slide 28: Activity recognition
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
Sliding window (2 s)
f1 | f2 | f3 | ... |  | Activity
Training
Machine learning
AR model
Average acceleration
Standard deviation of acceleration
Orientation
...
Manually
labelled

## Slide 29: Activity recognition
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
f1 | f2 | f3 | ... | 
Use/testing
Activity
Sliding window (2 s)
AR model

## Slide 30: Energy expenditure estimation
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate data
Sliding window (10 s)
Activity
AR model

## Slide 31: Energy expenditure estimation
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate data
Sliding window (10 s)
f’1 | f’2 | f’3 | ... |  | Activity | EE
Training
Machine learning (regression)
EEE model
Activity
AR model
Like for AR
Heart rate
Area under acceleration
Kinetic energy
...
Image copyright University of Porto

## Slide 32: Energy expenditure estimation
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate data
Sliding window (10 s)
f’1 | f’2 | f’3 | ... |  | Activity
Use/testing
EEE model
Activity
AR model
EE

## Slide 33: Stress detection
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate, GSR data
EEE model
EE
Sliding window (1 min)
f“1 | f“2 | f“3 | ... | History | Time | EE | Stress
Training
Machine learning (classification)
Heart rate variability features
GSR frequency features
Stress model
Image copyright QuestionPro

## Slide 34: Stress detection
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration, heart rate, GSR data
EEE model
EE
Sliding window (1 min)
f“1 | f“2 | f“3 | ... | History | Time | EE
Machine learning (classification)
Stress model
Use/testing
Stress

## Slide 35: Wellbeing monitoring
Stress
Stress model
Activity
AR model
EEE model
EE
Improvements:
Adaptation to the phone‘s location, orientation
Multiple models (for energy expenditure estimation, stress detection)
Deep learning
...

## Slide 36: Wearable example with deep learning

## Slide 37: Overview of the example
Sensing:
PPG
(Acceleration, temperature, GSR)
Processing:
Data cleaning
BP estimation
Image copyright Designmodo, Victorgrigas
MIMIC III
Sensing:
PPG

## Slide 38: Data cleaning (1)
Download PPG + continuous arterial BP data → 30,000 patients
Remove empty or obviously useless files → 10,000 patients
Remove files < 10 min
Standardize: mean = 0, std. dev = variance = 1
Band-pass filter: 4th order Butterworth filter with cut-off frequencies 0.5, 8 Hz

## Slide 39: Data cleaning (2)
Remove outliers (Hempel filter = version of median filter)
Remove anomalies in ground truth
→ 510 patients

## Slide 40: Preparing for deep learning
Original
Derived
5-second
windows

## Slide 41: DL architecture (1)
PPG
PPG‘
PPG‘‘
Spectro-temporal block
ResNet blocks
(CNN)
2 x dense
Spectro-temporal block
ResNet blocks
(CNN)
Spectro-temporal block
ResNet blocks
(CNN)
Concat.
Gated recurrent u. (GRU)
SBP
DBP

## Slide 42: DL architecture (2)
Convolution
Convolution
Convolution
Add
ResNet block
4 more ResNet blocks
Short- cut
Spectro-temporal block
Spectrogram
GRU

## Slide 43: Personalisation
Results unsatisfactory:
  Error 15.4/12.4 mmHg for SPB/DBP
  Dummy error 19.7/10.6 mmHg
Add each person‘s data to training set:
  Error 9.4/6.9 mmHg

## Slide 44: Mobile phone example

## Slide 45: Overview of the example
Sensing:
Acceleration
GPS
Wi-fi
Audio
Light
Call log
Charging, lock/unlock
(Application use)
Stress-relief recommendations
StudentLife
Processing:
Stress detection

## Slide 46: Feature extraction (1)
Short-term:
  Activity: percentage of active vs. stationary
  Sound: percentage of voice, noise, silence
  Time of day (day, evening, night)
Long-term:
  Activity, sound, combinations (e.g., stationary + silent)
  Distance travelled
  Live conversations
  Phone calls
... for each time of day,
relative to subject‘s average

## Slide 47: Feature extraction (2)
Sleep duration (from light and charging)
Current and previous location (from wi-fi)
Days before/after midterm

## Slide 48: Training and evaluation
Leave one subject out (LOSO):
  Take one subject for testing
  Train on other subjects
  Repeat for all subjects and average
Plain LOSO
Train on a cluster similar to the test subject
Use personalisation

## Slide 49: Smart environment example

## Slide 50: Overview of the example
Sensing:
Hardware
Virtual
Reason about:
Which sensor values are bad
Which actions improve them
Simulation
Ontology +
Reasoning
Environment recommendations:
Appropriate temperature
Good air quality
Simulate suggested actions
Recommend the best one
Image copyright Netatmo

## Slide 51: Sensing
Sensing:
Hardware
Virtual
Number of occupants
Windows opened/closed
Hardware sensor readings (CO2 and others)
Machine-learning model / heuristics
Indoor:
Temperature
Humidity
CO2
Outdoor:
Temperature
Humidity
Image copyright Netatmo

## Slide 52: Ontology + reasoning

## Slide 53: Simulation
Suggested actions
from the ontology + reasoning
Prediction of outcomes:
Temperature
Humidity
CO2
Evaluation of the predicted outcomes
Recommended action
–1
0
1
0
–1
History of sensor readings
Machine-learning / physics models

## Slide 54: Miscellaneous examples

## Slide 55: Remote PPG reconstruction
Color-based: https://youtu.be/-cgESNK-84w?t=133
Motion-based: https://youtu.be/EhZXDgG9oSk?t=24
Heart pushes blood to the periphery
Blood returns to the heart
Blood flow through the carotid pushes head up
Color intensifies
Color lightens
Head moves down
Exploited by color-based
remote PPG monitoring
Exploited by motion-based
remote PPG monitoring

## Slide 56: Radio-based activity recognition
Wang et al.: Modeling RFID signal reflection for contact-free activity recognition
Radio transmitter
Radio receiver
https://www.youtube.com/watch?v=FnK4QHj00nk

## Slide 57: Localization based on ceiling lights
https://youtu.be/mgEf7J_M0Qk?t=29
Hu et al.: Lightitude: Indoor positioning using uneven light intensity distribution
Fingerprint lights (intensity, flicker ...)
Match current light to fingerprints
Take into account
orientation, movement
Light intensity
Light intensity

## Slide 58: Human-computer interaction
https://youtu.be/gvWxqAcsDBM?t=19
Smart restaurant table
Contact-free haptic feedback
https://youtu.be/5f5Kk5RReUE
Virtual mirror as a natural user interface
https://youtu.be/ZiXOsJeILmQ

## Slide 59: Conclusion
Ambient intelligence = environment intelligently and unobtrusively responsive
Devices: wearable and ambient sensors ...
Methods: machine learning, symbolic reasoning, knowledge representation ...
Domains: health and wellbeing, comfort and energy consumption ...

## Slide 60: Literature (1)
Physical monitoring with wearable sensors + machine learning: Cvetković et al., Real-time activity monitoring with a wristband and a smartphone, Information Fusion 2018
Psychological monitoring with wearable sensors + machine learning: Gjoreski et al., Monitoring stress with a wrist device using context, Journal of Biomedical Informatics 2017
Ambient sensors + symbolic reasoning: Alirezaie et al., An ontology-based context-aware system for smart homes: E-care@home, Sensors 2017

## Slide 61: Literature (2)
Audio + deep learning: Georgiev et al., Low-resource multi-task audio sensing for mobile and embedded devices via shared deep neural network representations, Ubicomp 2017
Indoor localization: Zafari et al., A Survey of indoor localization systems and technologies, 2018
Internet of Things: Al-Fuqaha et al., Internet of Things: A survey on enabling technologies, protocols, and applications, IEEE Communication Surveys & Tutorials 2015

## Slide 62: Literature (3)
Human-computer interaction: Hui & Sherratt, Towards disappearing user interfaces for ubiquitous computing: Human enhancement from sixth sense to super senses, Journal of Ambient Intelligence and Humanized Computing 2017