## Slide 1: Energy expenditure estimation with wearable accelerometers
Mitja Luštrek,
Božidara Cvetković and Simon Kozina
Jožef Stefan Institute
Department of Intelligent Systems
Slovenia

## Slide 2: Introduction
Motivation:
  Chiron project – monitoring of congestive heart failure patients
  The patient’s energy expenditure (= intensity of movement) provides context for heart activity

## Slide 3: Introduction
Motivation:
  Chiron project – monitoring of congestive heart failure patients
  The patient’s energy expenditure (= intensity of movement) provides context for heart activity
Method:
  Two wearable accelerometers → acceleration
  Acceleration → activity
  Acceleration + activity → energy expenditure
Machine
learning

## Slide 4: Measuring human energy expenditure
Direct calorimetry
  Heat output of the patient
  Most reliable, laboratory conditions

## Slide 5: Measuring human energy expenditure
Direct calorimetry
  Heat output of the patient
  Most reliable, laboratory conditions
Indirect calorimetry
  Inhaled and exhaled oxygen and CO2
  Quite reliable, field conditions, mask needed

## Slide 6: Measuring human energy expenditure
Direct calorimetry
  Heat output of the patient
  Most reliable, laboratory conditions
Indirect calorimetry
  Inhaled and exhaled oxygen and CO2
  Quite reliable, field conditions, mask needed
Diary
  Simple, Unreliable, patient-dependant

## Slide 7: Measuring human energy expenditure
Direct calorimetry
  Heat output of the patient
  Most reliable, laboratory conditions
Indirect calorimetry
  Inhaled and exhaled oxygen and CO2
  Quite reliable, field conditions, mask needed
Diary
  Simple, Unreliable, patient-dependant
Wearable accelerometers

## Slide 8: Hardware
Co-located with ECG
One placement
to be selected

## Slide 9: Hardware
Co-located with ECG
One placement
to be selected
Shimmer sensor nodes
3-axial accelerometer @ 50 Hz
Bluetooth and 802.15.4 radio
Microcontroller
Custom firmware

## Slide 10: Hardware
Co-located with ECG
One placement
to be selected
Shimmer sensor nodes
3-axial accelerometer @ 50 Hz
Bluetooth and 802.15.4 radio
Microcontroller
Custom firmware
Android smartphone
Bluetooth

## Slide 11: Training/test data
Activity
Lying
Sitting
Standing
Walking
Running
Cycling
Scrubbing the floor
Sweeping
...

## Slide 12: Training/test data
Activity | Energy expenditure
Lying | 1.0 MET
Sitting | 1.0 MET
Standing | 1.2 MET
Walking | 3.3 MET
Running | 11.0 MET
Cycling | 8.0 MET
Scrubbing the floor | 3.0 MET
Sweeping | 4.0 MET
... | 
1 MET =
energy
expended
at rest
Recorded
by five
volunteers

## Slide 13: Machine learning procedure
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
Sliding window (2 s)

## Slide 14: Machine learning procedure
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
Sliding window (2 s)
f1 | f2 | f3 | ... |  | Activity
Training
Machine learning
AR Classifier

## Slide 15: Machine learning procedure
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
f1 | f2 | f3 | ... | 
Use/testing
Activity
Sliding window (2 s)
AR Classifier

## Slide 16: Machine learning procedure
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
Activity
AR Classifier

## Slide 17: Machine learning procedure
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
Sliding window (10 s)
Activity
AR Classifier

## Slide 18: Machine learning procedure
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
Sliding window (10 s)
f’1 | f’2 | f’3 | ... |  | Activity | EE
Training
Machine learning (regression)
EEE Classifier
Activity
AR Classifier

## Slide 19: Machine learning procedure
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
Sliding window (10 s)
f’1 | f’2 | f’3 | ... |  | Activity
Use/testing
EEE Classifier
Activity
AR Classifier
EE

## Slide 20: Machine learning procedure
at | at+1 | at+2 | ... |  |  |  |  |  |  |  | 
Acceleration data
EE
Energy expenditure

## Slide 21: Features for activity recognition
Average acceleration
Variance in acceleration
Minimum and maximum acceleration
Speed of change between min. and max.
Accelerometer orientation
Frequency domain features (FFT)
Correlations between accelerometer axes

## Slide 22: Features for energy expenditure est.
Activity
Average length of the acceleration vector
Number of peaks and bottoms of the signal

## Slide 23: Features for energy expenditure est.
Activity
Average length of the acceleration vector
Number of peaks and bottoms of the signal
Area under acceleration
Area under gravity-subtracted acceleration

## Slide 24: Features for energy expenditure est.
Activity
Average length of the acceleration vector
Number of peaks and bottoms of the signal
Area under acceleration
Area under gravity-subtracted acceleration
Change in velocity
Change in kinetic energy

## Slide 25: Sensor placement and algorithm
 | Linear regression | Support vector regression | Regression tree | Model tree | Neural network
Chest + ankle | 5.09 | 3.29 | 1.41 | 2.18 | 1.65
Chest + thigh | 6.75 | 3.68 | 1.58 | 2.38 | 1.66
Chest + wrist | 6.75 | 3.94 | 1.30 | 4.95 | 1.39
Mean absolute error in MET

## Slide 26: Sensor placement and algorithm
 | Linear regression | Support vector regression | Regression tree | Model tree | Neural network
Chest + ankle | 5.09 | 3.29 | 1.41 | 2.18 | 1.65
Chest + thigh | 6.75 | 3.68 | 1.58 | 2.38 | 1.66
Chest + wrist | 6.75 | 3.94 | 1.30 | 4.95 | 1.39
Mean absolute error in MET

## Slide 27: Sensor placement and algorithm
 | Linear regression | Support vector regression | Regression tree | Model tree | Neural network
Chest + ankle | 5.09 | 3.29 | 1.41 | 2.18 | 1.65
Chest + thigh | 6.75 | 3.68 | 1.58 | 2.38 | 1.66
Chest + wrist | 6.75 | 3.94 | 1.30 | 4.95 | 1.39
Mean absolute error in MET

## Slide 28: Sensor placement and algorithm
 | Linear regression | Support vector regression | Regression tree | Model tree | Neural network
Chest + ankle | 5.09 | 3.29 | 1.41 | 2.18 | 1.65
Chest + thigh | 6.75 | 3.68 | 1.58 | 2.38 | 1.66
Chest + wrist | 6.75 | 3.94 | 1.30 | 4.95 | 1.39
Mean absolute error in MET

## Slide 29: Sensor placement and algorithm
 | Linear regression | Support vector regression | Regression tree | Model tree | Neural network
Chest + ankle | 5.09 | 3.29 | 1.41 | 2.18 | 1.65
Chest + thigh | 6.75 | 3.68 | 1.58 | 2.38 | 1.66
Chest + wrist | 6.75 | 3.94 | 1.30 | 4.95 | 1.39
Mean absolute error in MET

## Slide 30: Sensor placement and algorithm
 | Linear regression | Support vector regression | Regression tree | Model tree | Neural network
Chest + ankle | 5.09 | 3.29 | 1.41 | 2.18 | 1.65
Chest + thigh | 6.75 | 3.68 | 1.58 | 2.38 | 1.66
Chest + wrist | 6.75 | 3.94 | 1.30 | 4.95 | 1.39
Mean absolute error in MET

## Slide 31: Sensor placement and algorithm
 | Linear regression | Support vector regression | Regression tree | Model tree | Neural network
Chest + ankle | 5.09 | 3.29 | 1.41 | 2.18 | 1.65
Chest + thigh | 6.75 | 3.68 | 1.58 | 2.38 | 1.66
Chest + wrist | 6.75 | 3.94 | 1.30 | 4.95 | 1.39
Mean absolute error in MET
Lowest error, poor extrapolation, interpolation
Second lowest error, better flexibility

## Slide 32: Estimated vs. true energy
Average
error:
1.39 MET

## Slide 33: Estimated vs. true energy
Low intensity
Moderate
intensity
Running, cycling
Average
error:
1.39 MET

## Slide 34: Estimated vs. true energy
Low intensity
Moderate
intensity
Running, cycling
Average
error:
1.39 MET

## Slide 35: Multiple classifiers
Activity
AR Classifier

## Slide 36: Multiple classifiers
Activity
AR Classifier
General
EEE Classifier
EE
Cycling
EEE Classifier
Running
EEE Classifier
Activity = cycling
Activity = running
Activity = other

## Slide 37: Estimated vs. true energy, multiple cl.
Low intensity
Moderate
intensity
Running, cycling
Average
error:
0.91 MET

## Slide 38: Conclusion
Energy expenditure estimation with wearable accelerometers using machine learning
Study of sensor placements and algorithms
Multiple classifiers: error 1.39 → 0.91 MET

## Slide 39: Conclusion
Energy expenditure estimation with wearable accelerometers using machine learning
Study of sensor placements and algorithms
Multiple classifiers: error 1.39 → 0.91 MET
Cardiologists judged suitable to monitor congestive heart failure patients
Other medical and sports applications possible